## Slide 1: Reducing Forks in the Blockchain via Probabilistic Verification
Bing Liu, Yang Qin and Xiaowen Chu
Harbin Institute Technology(Shenzhen)&Hong Kong Baptist University
liubing@stu.hit.edu.cn
April 8, 2019

## Slide 2: Outline
1. Motivation
  The generation of forks
  The harm of forks
2. Block Propagation Delay
3. Probabilistic Verification
  PvScheme
  Enhanced PvScheme
  Security Analysis
4. Experiments and Results
5. Conclusion

## Slide 3: 1.Motivation
The generation of forks
The blockchain forks are mainly caused by the block propagation delay in the network.
To some degree, it can reduce forks if we can reduce block propagation delay.
Fig.1 Forks in blockchain
But what if B31 travels faster, and reaches M6 before B32 is created?

## Slide 4: 1.Motivation
The harm of forks
(1) The emergence of fork wastes the computing power of the network.
(2)The fork weakens the security of blockchain, and increases the risk of attacks and double-spending.
(3) The computing capacity of network is actually split, which will directly
reduce the production rate of blocks and affect the system’s performance.
(4) The fork will delay the time the transaction is confirmed.

## Slide 5: 2.Block Propagation Delay
  The propagation delay is the combination of transmission time and the time of local verification of the block.
  The verification time is the major contributor to the propagation delay.
  The improvement of the verification time will greatly improve the efficiency for peers to receive blocks, which will reduce the blockchain forks in some degree.
Fig. 2 The process of block propagation

## Slide 6: 3.Probabilistic Verification
PvScheme: In probabilistic verification, a node does not need to verify each block it has received, but selectively verifies blocks based on a probability.
Validation degree υ: the average block verification ratio of nodes in blockchain.
E.g. when the validation degree is 0.5, a block is verified every two nodes on average across the network.
When the validation degree is 1, the node needs to verify each block, which is the standard protocol implemented now.

## Slide 7: 3.Probabilistic Verification
PvScheme
If the probability ε meets the validation degree υ, the block does not need to be verified and is accepted directly.
Otherwise, the block needs to be verified.
Fig. 3. The process of probabilistic verification
verification flag

## Slide 8: 3.Probabilistic Verification
  Enhanced PvScheme
  (1)Feedback and rebroadcast
  Cause : When the validation degree is not 1, blocks are not strictly verified by nodes. There may be some fake blocks that have accepted by some nodes.
  Purpose: To ensure a reliable block delivery

## Slide 9: 3.Probabilistic Verification
Feedback and rebroadcast design
When a node verifies a block and finds an error,
it continues to feedback until it finds a node with the validated block,
and requires the node to rebroadcast the block.
Fig. 4. The process of feedback and rebroadcast
verification flag

## Slide 10: 3.Probabilistic Verification
  Enhanced PvScheme
  (2) Threshold
  Cause: In the worst case, all nodes may accept a block without verification.
  To avoid the worst case, we set threshold value θ≤3, which means three consecutive nodes at most are allowed to accept the block without verification.
  Purpose: a. In order to detect fake blocks as quickly as possible. b. If there is an error, the block can be retransmitted in a shorter path.

## Slide 11: 3.Probabilistic Verification
Security Analysis
Fake blocks
Tnew : the propagation delay in the PvScheme.
Tsta : the propagation delay in the standard protocol.
p: the probability of a block error at the validation degree υ.
transmission time tm, verification time tv, the feedback time tf at a hop, and
tv >>tm>>tf
1/υ : the average feedback path length at the validation degree υ
(1) In the standard protocol, the propagation delay Tsta is the combination of the transmission time tm and verification time tv.
(2)In PvScheme, the feedback time and rebroadcast time should also be included.

## Slide 12: 3.Probabilistic Verification
Security Analysis
Fake blocks
Solution: our scheme costs less propagation delay than the standard protocol if less than 50% error blocks occurs in the validation degree of 0.5, or less than 10% error blocks occurs in the validation degree of 0.9.
We would like to know the range of p, which makes the propagation delay of PvScheme is still less than the delay of the standard protocol. Make Tnew =Tsta, and we get:
When υ=0.5,we get p=0.5, and υ=0.9, we get p=0.1 .
That is:
When υ=0.9, if p<0.1, Tnew < Tsta When υ=0.9, if p>0.1, Tnew > Tsta

## Slide 13: 4.Experiments and Results
PvScheme
 | Definition
validation degree υ | the average block verification ratio of nodes in blockchain
synchronization time τ | the delay required for all nodes to fully accept blocks in the network
stale block rate rs | the ratio of stale blocks to total blocks over a given period of time - It measures how many forks there are.
security index ς | the level of safety in which blocks are not tampered with at the current validation degree
security assessment rate ρ | a joint analysis of the block security and performance at various validation degrees,

## Slide 14: 4.Experiments and Results
PvScheme: We want to get a lower stale block rate as safely as possible. The security assessment rate ρ is expressed as
In theory, the greater the validation degree υ, the more nodes need
to verify the block. Therefore, it costs more block propagation delays,
resulting in a larger synchronization time τ and stale block rate rs.
In practice, we need a smaller synchronization time τ and stale block rate rs, as well as a larger security index ς. Therefore, we ask for a smaller ρ in this formula.

## Slide 15: 4.Experiemnts and Results
In order to consider the tradeoff between security and performance in blockchain, we set the validation degree υ from 0.5 to 1 in our experiments.

## Slide 16: 4.Experiemnts and Results
In this experiment, 1000 blocks were designed to be broadcast between 6000 nodes.
In Figure 5 and Figure 6, as validation degree increases, so does the synchronization time and the stale block rate, which is consistent with our previous theoretical analysis.
By contrast, after enhancing PvScheme security, PvScheme has higher synchronization time and stale block rate than before. Since the security design increases the delay of the system.
Fig. 5. Synchronization time under various validation degrees
Fig. 6.Stale block rate under various validation degrees

## Slide 17: 4.Experiemnts and Results
Figure 7 shows the propagation delay of blocks received by different proportions of nodes in the network at various validation degrees.
The block propagation delay increases with the increase of the validation degree. It is still in accordance with our analysis. More propagation delay occurs because more nodes verify the block.

## Slide 18: 4.Experiemnts and Results
We also have captured the longest continuous forks at various validation degrees.
As validation degree increases, in addition to the validation degree of 0.9, the longest forks also show an increasing trend. It means PvScheme can indeed reduce the number of continuous forks.
The generation of fork is inherently random, so the data in the validation degree of 0.9 is normal.

## Slide 19: 4.Experiemnts and Results
Here, we get experimental results under various validation degrees.
In TABLE II, it meets the requirements when the validation degree υ =0.9.
Solution: we can use the validation degree of 0.9, that is, 9 verifications out of 10 nodes to replace the standard protocol.
Based on the above theoretical analysis, we need to find the minimum security assessment rate ρ.

## Slide 20: 5.Conclusion
According to our experimental simulations, we get the best effect when the validation degree is 0.9. It gets a relatively low fork and a relatively high level of security at the same time, which achieves a compromise between the performance and security in blockchain.
In practice, it should be combined with reality to determine the most reasonable value of validation degree. It can be determined that the most reasonable value of validation degree is various for different environments and network structures.

## Slide 21
Please email your questions to: liubing@stu.hit.edu.cn
Thank You !!